## Slide 1: Factor Graphs and Nonlinear Least-Squares Problems on Manifolds
June 6 2017
Pranav Ganti

## Slide 2: Outline
Overview
Factor Graphs
Least Squares
Nonlinear Least Squares
NLLS – extended to Manifolds!

## Slide 3: Overview
SLAM is an optimization problem
Given many measurements, what is the value of the parameters we are trying to estimate?
  Overdetermined system
Want to estimate the state, using the incoming measurements
  Nonlinear
  SE(3) or SE(2)

## Slide 4: Overview | Assumptions
Independent
  Previous sensory information does not affect the next reading
Identically Distributed
  Sensor noise distribution is unchanged between samples
  Gaussian

## Slide 5: Overview | Likelihood and Posterior
Likelihood
Posterior
Notes: Posterior dist is the probability of a random quantity, conditional on evidence. After taking relevant info into account.
Posterior is proportional to the likelihood

## Slide 6: Overview | ML and MAP
ML – Maximum Likelihood
MAP – Maximum A Posteriori
Notes: MLE is a special case of MAP, assuming a uniform prior (or ignores prior)

## Slide 7: Factor Graphs
Probabilistic model which illustrates the factorization of a function
Highlights conditional dependence between random variables
Bipartite – graph has two distinct nodes
  Classified into variables and factors
  Connected together by edges
Excels in problems such as SLAM or SFM

## Slide 8: Factor Graphs | Variables and Factors
Variables are the parameters that we are looking to optimize.
  For SLAM: the robot (and landmark) poses.
Factors are probability statements
  Highlight the constraints between variables (conditional dependence)
  Derived from measurement or mathematical fundamentals
  For SLAM: odometry, reprojection error, GPS measurements, etc.

## Slide 9: Factor Graphs | Example
  are robot poses over 3 time steps
  is the prior
    Unary factor
  are odometry measurements
    Binary factor
Notes: Unary ex. GPS
Binary ex. Lidar measurements

## Slide 10: Factor Graphs | Example – Loop Closure
Notes: SLAM is extremely dependent on correct loop closures. An incorrect correspondence can cause divergence
Factor graph does not take care of ANY of this; that’s all front end. This is effectively just the back-end optimization
However, the addition of a constraint between poses 5 and 2 will close the loop.

## Slide 11: Factor graphs | Board Example
Let’s draw a factor graph with:
  3 timesteps
  2 landmarks
  Odometry
  LIDAR measurements to landmarks

## Slide 12: Factor Graphs | Answer

## Slide 13: Factor Graphs | Graphs vs. Value
The value of the factor graph is the product of all factors.
Maximizing the value is equivalent to the MAP estimation.
  The prior is already included as a factor.
  Recall:
Notes: Discussion regarding inclusion of multiple priors vs just 1.

## Slide 14: Factor Graphs | Notes
The graph describes the posterior density over the full trajectory of the robot
The graph does not contain a solution
  The graph is a function, applied to the parameters
An initial guess + nonlinear least squares can be used to find the MAP estimate for the trajectory

## Slide 15: Factor Graphs | SLAM Application
The graph consists of:
  100 poses
  30 landmarks
Using GTSAM with an initial guess solves for the full pose estimate of the robot and landmarks
  Also includes covariances

## Slide 16: Factor Graphs | Example
Notes: 517 factors
119 multivariate variables
Optimizes in < 10 ms
From Victoria Park dataset

## Slide 17: Factor Graphs | Batch Estimation vs. Sliding Window
Batch Estimation
  Optimize over all poses in the trajectory

## Slide 18: Factor Graphs | Batch Estimation vs. Sliding Window
Sliding window
  Optimize only over poses in the window

## Slide 19: Factor Graphs | Batch Estimation vs. Sliding Window
Sliding window
  Optimize only over poses in the window
  All previous information is encoded in as a prior

## Slide 20: Factor Graphs | Other Applications
Visual Odometry
  Pose constraints provided by tracking features
Visual SLAM
  Extension of VO, to observing 3D points with mapping and loop closure
Fixed-lag Smoothing and Filtering
  Recursive estimation – only require a subset of the poses
  Can marginalize for online estimation
Discrete Variables and Hidden Markov Models
Notes: Fixed –lag: only incorporates x previous poses
GTSAM specific applications

## Slide 21: Least Squares
Purpose: to solve an overdetermined system of equations.
Review:

## Slide 22: Linear vs Nonlinear Least Squares
Linear:
Nonlinear:

## Slide 23: Nonlinear Least Squares
Not all factors are linear wrt the parameters.
  Odometry, reprojection error, etc.
Main idea: linearize model about current parameters and refine
Let us work through the derivation:
Notes: Discuss probability of measurement is Gaussian, taking ERROR means just shifting the Gaussian. Information/covariance stays the same.

## Slide 24: Nonlinear Least Squares | Derivation
The measurement (and therefore error) can be expressed as (Gaussian Assumption)
  Error has zero mean, with Information Matrix
Remove the minus: (does this equation look familiar)?

## Slide 25: Nonlinear Least Squares | Derivation
Let
Therefore, the argument of minimization is:
We can take the first-order Taylor Approximation of the error function
  Taken about the initial guess
  is the Jacobian at the guess.

## Slide 26: Nonlinear Least Squares | Derivation
Inserting this into the error function yields:
Substitute error definition

## Slide 27: Nonlinear Least Squares | Derivation
Multiplying the terms and expanding yields:
Which looks quite familiar!
We can solve this!

## Slide 28: Nonlinear Least Squares | Derivation
The error function is the sum over all timesteps
  Expressed as:

## Slide 29: Nonlinear Least Squares | Derivation
The final step is to take the derivative, and set to zero.
This yields:
And the next iteration occurs at:
  Until the convergence condition is met

## Slide 30: Gauss-Newton and Levenberg-Marquardt
This is the Gauss-Newton algorithm.
  However, sometimes Gauss-Newton can lead to worse estimates
Levenberg-Marquardt is a damped () version of the Gauss-Newton algorithm
  Introduces contingency to recover from a worse estimate
  As moves to , moves to
    Controls size of increments

## Slide 31: Structure
Both SLAM and Bundle Adjustment have a characteristic structure
  Sparsity
  Only non-zero between poses connected by a constraint
    = 2x # of constraints + # of nodes
We can exploit this structure to solve

## Slide 32: Structure | Jacobian
From:
The Jacobian can be expressed as:
Each corresponds to the derivative wrt the nodes connected by the kth edge

## Slide 33: Structure | Hessian
By setting
  W
  s

## Slide 34: Structure | Solving
This can now be solved by Sparse Cholesky Factorization
  Cholesky decomposition:
Solvers:
  CSparse
  CHOLMOD
  Preconditioned Gradient (PCG)
    Only if system is too large

## Slide 35: NLLS on Smooth Manifolds
The previous derivation assumes the parameters are Euclidean
  Not true for SLAM
  Pose estimates are SE(3)
Box-plus and box-minus

## Slide 36: NLLS on Smooth Manifolds | Problem Structure
Recall: taking Taylor expansion of error near initial guess
  Now, we must look at a perturbation

## Slide 37: NLLS on Smooth Manifolds | Substitution
Replace addition with box plus, and subtraction with box-minus
Substitute error definition with box-plus and box-minus

## Slide 38: NLLS on Smooth Manifolds | Solving
The Jacobian takes on the form:
The remaining steps are just an extension of the Euclidean derivation
  Solution does depend on implementation of box-plus and box-minus

## Slide 39: NLLS on Smooth Manifolds | Notes
Linearized manifold representation has the same structure as Euclidean case
Steps:
  Compute set of increments in local Euclidean approximation
Libraries such as GTSAM and g2o incorporate this functionality, as they are designed for SLAM

## Slide 40: Homework
Draw a factor graph with the following:
  5 timesteps
  6 landmarks
  GPS measurements at each timestep
  Odometry
  IMU (at same frequency as odometry)
  LIDAR measurements to each landmark
  Reprojection error

## Slide 41: References
Course References
[1] R. Kümmerle, G. Grisetti. H. Strasdat, K. Konolige, and W. Burgard, “g 2 o: A general framework for graph optimization,” in Robotics and Automation (ICRA), 2011 IEEE International Conference on, pp. 3607-3613, IEEE, 2011.
[2] F. Dellaert, “Factor graphs and gtsam: A hands-on introduction,” tech.rep., Georgia Institute of Technology, 2012.
Additional References
[3] M. Kaess, A. Ranganathan, and F. Dellaert, “isam: Incremental smoothing and mapping,” IEEE Transactions on Robotics, vol. 24, no. 6, pp. 1365-1378, 2008.
[4] G. Grisetti, R. Kümmerle, C. Stachniss, and W. Burgard, “A tutorial on graph-based SLAM,” IEEE Intelligent Transportation Systems Magazine, vol. 2, no. 4, pp. 31-43, 2010.
[5] G. Grisetti, “Notes on Least-Squares and SLAM DRAFT,” 2015. Retrieved from http://www.dis.uniroma1.it/~grisetti/teaching/lectures-ls-slam-master_2015_16/web/reading_material/grisetti12stest.pdf

## Slide 42: References…cont
[6] C. Stachniss, “Least squares approach to SLAM.” Lecture Slides, University of Freiburg. Retrieved from http://ais.informatik.uni-freiburg.de/teaching/ws12/mapping/pdf/slam15-ls-slam.pdf
[7] W. Burgard, C. Stachniss, K. Arras, M. Bennewitz, “Advanced Techniques for Mobile Robotics – Least Squares.” Lecture Slides, University of Freiburg. Retrieved from http://ais.informatik.uni-freiburg.de/teaching/ws11/robotics2/pdfs/rob2-06-least-squares.pdf.
All images retrieved from wikipedia.org.